# Method: Substrate and Depth

# Note: This method must be preceded by the Transects Method at each Primary Transect

# For Waded Streams:

# Identify Stations

One person working along a primary transect (each of these transects: A0, B0, C0, D0, E0, F0, G0, H0, I0, J0, K0) collects information about each of 11 equidistant points on the substrate: depth, substrate type, and embeddedness.

For example, Transect A0 TransectStationLeftRightID would be labeled as follows:

A000-Left bank

A001-1/10th the distance from left to right bank

A002-2/10ths the distance, etc

A010-The complete distance (10 tenths) from left to right bank.

Measure Depth

Depth is measured with a surveyor’s rod to the nearest cm. Record either the WettedDepth (cm) or the BankfullDepth (cm), whichever is easiest. Negative values are allowed for particles that extent out of the wetted surface. A hand level may be used to help determine the height of bankfull stage relative to the surveyor’s rod.

________________________________________________________________________

Estimate Embeddedness

At each station, touch the nearest particle to foot of the surveyor’s rod then look at it. Estimate Embeddedness (%). This is the fraction of a particle’s surface that is surrounded by (embedded in) fine sediments (≤ 2 mm).  Particles smaller than 100 mm are evaluated using a 10 cm ring surrounding the sample point. All particles within the ring are evaluated for size and embeddedness, not just the point. Record the estimated average for surface substrate within the ring.  By default, sand or fines are 100% embedded.  By default, bedrock is 0% embedded.
________________________________________________________________________

Classify Substrate

Estimate the particle size class for the sample point. Record the SubstrateTypeCode. These are as follows:

RS - Bedrock (smooth) - larger than a car

RR - Bedrock (rough) - larger than a car

RC - Concrete/Asphalt

XB - Large Boulder – (1 m to 4 m) meter stick to car

SB -  Small boulder (250 mm to 1 m) basketball to meter stick

CB - Cobble (64 to 250 mm) tennis ball to basketball

GC - Gravel, coarse (16-64 mm) marble to tennis ball

GF - Gravel, fine (2-16 mm) ladybug to marble

SA - Sand (2-16 mm) gritty to ladybug

FN - Fines (silt/clay/muck) non gritty

HP - Hardpan - hardened soil, chemically cemented together

HS - Hardsand - sand consolidated by vegetation or physical conditions (rare)

WD - Wood – any size

OT – Other (describe in comments)

For GF, GC, and CB, use calipers to confirm your estimate.

For Rafted Rivers

To assist estimates in rafted rivers, crews will make use of averaging techniques from 20m x 10m littoral plots. Crews will work from only one bank at each primary transect.

At each dry TransectStationLeftRightID record bankfull depth and substrate information, as for wadeable streams.

Where the transect crosses 10 m into the wetted channel, estimate the dominant substrate for a 20 m length of stream – record the appropriate SubstrateTypeCode, and the average Embeddedness. Record these data in the space for the most-streamward left-to-right station (TransectStationLeftRight) within the littoral plot. Measure the WettedDepth (cm) at that station with a sonar or rod. Except for dry or shallow portions of the transect, particles might not be handled during raft work.

| Platform | Station | Station description |
| --- | --- | --- |
| Wade | 00 | Left bank (bankfull) |
| Wade | 01 | 10% distance from left to right |
| Wade | 02 | 20% distance from left to right |
| Wade | 03 | 30% distance from left to right |
| Wade | 04 | 40% distance from left to right |
| Wade | 05 | 50% distance from left to right |
| Wade | 06 | 60% distance from left to right |
| Wade | 07 | 70% distance from left to right |
| Wade | 08 | 80% distance from left to right |
| Wade | 09 | 90% distance from left to right |
| Wade | 10 | Right bank (bankfull) |
| Platform | Station | Station description |
| Raft | 00 or 10 | Left bank or Right bank |
| Raft | Varies | All dry stations on that side of bank |
| Raft | Varies | Most streamward station in littoral plot |