# Method: Human Influence

One person working at each bank of a primary transect collects information relative to a 10m x 10m plot (waded streams)  or relative to a 10m x 20m plot (rafted rivers) that is centered on the transect and extends from the bankfull margin landward.

Record TransectID (one of these: A0, B0, C0, D0, E0, F0, G0, H0, I0, J0, K0) at the top of the form. Determine which Direction Observed column to complete: either left bank (LB) or right bank (RB).

Then assess the presence and proximity of each of 13 InfluenceTypes.

Record the appropriate InfluenceProximity code next to each.

Human Influence Type

Buildings

Landfill/trash

Logging

Mining

Park/Lawn

Pasture/Range/Hay Field

Paved Road/Railroad

Unpaved Road/Motor Trail

Footpath (human)

Open Lot (Paved or Cleared)

Pipes

Row Crops

Wall/Dike/Revetment

| Influence Proximity | Code Description |
| --- | --- |
| 0 | Absent |
| 1 | Beyond the plot, but within 30 m of bankfull margin |
| 2 | Within the 10 x10 m plot |
| 3 | On the bank or in the bankfull channel |