# Method: Riparian Vegetation Structure

One person working at each bank of a primary transect collects information relative to a 10m x 10m plot that is centered on the transect and extends from the bankfull margin landward.

Record TransectID (one of these: A0, B0, C0, D0, E0, F0, G0, H0, I0, J0, K0) at the top of the form. Determine which Direction Observed column to complete: either left bank (LB) or right bank (RB).

Then assess vegetation type and shade in the plot. Consider each of 3 layers:

- Ground Cover ______	0-0.5 m high (to ankle height)

- Under Story: _______Between 0.5m and 5 m height

- Canopy:___________Over 5 m high

Start with Canopy

- Record the code for VegType.

| Code | VegType |
| --- | --- |
| D | Deciduous |
| C | Coniferous |
| E | Broadleaf Evergreen (e.g. Arbutus menziesii) |
| M | Mixed |
| N | None |

- Record the PercentCoverCode next to each of 2 VegLifeForms for Canopy: Big Trees, Small Trees.

| Code | Cover (%) |
| --- | --- |
| 0 | 0 |
| 1 | < 10 |
| 2 | 10-40 |
| 3 | 40-75 |
| 4 | > 75 |

Proceed to Under Story

- Record the code for VegType : (D)eciduous, (C)oniferous, (E)vergreen-broadleaf, (M)ixed, or (N)one.

- Record the PercentCoverCode next to each of 2 VegLifeForms for Under Story: Woody, Non-woody.

Proceed to Groundcover

- There is no VegType for Ground Cover.

- Record the PercentCoverCode next to each of 3 VegLifeForms for Groundcover: Woody, Non-woody, Bare.