# Method: Thalweg

# For Waded Streams:

One person walking upstream evaluates characteristics of the stream at each of 101 longitudinal stations (Thalweg stations), that are labeled 0-9 for each transect letter (A-J) plus K0.

- Thalweg Depth (cm)

- Characterize BarPresent with Y/N

- Characterize  BackwaterPresent and SidepoolPresent each with Y/N.

- Identity of each Habitat UnitNumber (cumulative count for the entire site A-K)

- Identify each side channel with a SideChannelNumber (cumulative count for the entire site A-K)

At every secondary transect (A5, B5, C5, D5, E5, F5, G5, H5, I5, J5) widths are measured:

- WettedWidth

- BankfullWidth

- BarWidth

For Rafted Rivers

Float downstream and make these modifications to the above protocol:

- Thalweg Depth (cm) – estimated average for the segment (e.g. A0 to A9) using at least one sonar measurement. Average value recorded at Station A5.

No secondary transect widths are measured.