# Method: Substrate – Secondary Transects

# Note: This method must occur during the Thalweg Method and only occurs for waded streams

# For Waded Streams:

# Identify Stations

One person working along a secondary transect (each of these transects: A5, B5, C5, D5, E5, F5, G5, H5, I5, J5) collects information about each of 11 equidistant points on the substrate: substrate type.

For example, Transect A5 TransectStationLeftRightID would be labeled as follows:

A500-Left bank

A501-1/10th the distance from left to right bank

A502-2/10ths the distance, etc

A510-The complete distance (10 tenths) from left to right bank.

Classify Substrate

Estimate the particle size class for the sample point. Record the SubstrateTypeCode. These are as follows:

RS - Bedrock (smooth) - larger than a car

RR - Bedrock (rough) - larger than a car

RC - Concrete/Asphalt

XB - Large Boulder – (1 m to 4 m) meter stick to car

SB -  Small boulder (250 mm to 1 m) basketball to meter stick

CB - Cobble (64 to 250 mm) tennis ball to basketball

GC - Gravel, coarse (16-64 mm) marble to tennis ball

GF - Gravel, fine (2-16 mm) ladybug to marble

SA - Sand (2-16 mm) gritty to ladybug

FN - Fines (silt/clay/muck) non gritty

HP - Hardpan - hardened soil, chemically cemented together

HS - Hardsand - sand consolidated by vegetation or physical conditions (rare)

WD - Wood – any size

OT – Other (describe in comments)

For GF, GC, and CB, use calipers to confirm your estimate.

| Platform | Station | Station description |
| --- | --- | --- |
| Wade | 00 | Left bank (bankfull) |
| Wade | 01 | 10% distance from left to right |
| Wade | 02 | 20% distance from left to right |
| Wade | 03 | 30% distance from left to right |
| Wade | 04 | 40% distance from left to right |
| Wade | 05 | 50% distance from left to right |
| Wade | 06 | 60% distance from left to right |
| Wade | 07 | 70% distance from left to right |
| Wade | 08 | 80% distance from left to right |
| Wade | 09 | 90% distance from left to right |
| Wade | 10 | Right bank (bankfull) |