Method: Large Woody Debris

Waded Streams

One person, while walking upstream, counts the number of pieces of large woody debris (LWD), that are within the bankfull channel of each stream segment (e.g. A0 to B0). Pieces are tallied according to 12 size classes (4 diameter classes and 3 length classes) that match those of the EMAP-West program.

Rafted Rivers

One person, while floating downstream, stops at each primary transect. At each primary transect they assess a plot on one side of the river. They count the number of pieces of large woody debris (LWD), that are within the bankfull channel of a plot that extends 20 m along the length of the stream (centered on the transect). The plot extends 10 m into the river.